## Slide 1: Resilience Assessment Toolkit
Storm Reconstruction and DER Integration
Prepared for
December 16, 2020

## Slide 2: Agenda – December 16, 2020
Q&A
DER Integration
Storm Reconstruction
Introductions

## Slide 3: Introductions
Erik Gilbert
Director
Brett Feldman
Research Director
Michael Hartnack
Senior Research Analyst
The Guidehouse Team

## Slide 4: Storm Reconstruction

## Slide 5: Executive Summary
Utilities must challenge existing models and regulatory constructs, and pursue innovative spending strategies and revenue initiatives to adapt their business to the growing natural challenges.
Overall community safety during a storm and resiliency after a storm is closely tied to the condition and status of the electric power grid, and operators must realize this when prioritizing reliability and resiliency grid investments for storm reconstruction.
Vendors must rise to the challenge of providing utilities with cutting-edge technology which solves critical utility issues today and works to address those of the future.
The core principal of any major reconstruction effort should be to rebuild smart, ensuring that reconstruction funds maximize the deployment of innovative and dynamic technologies to mitigate future power outages, save lives, and protect property.
T&D grids are dynamic, challenging, and critical utility assets. The continued integration of advanced technologies for resiliency, restoration, and storm reconstruction is critical to managing the effects of a growing trend in storm and natural disaster frequency, cost, and scale.

## Slide 6: Resiliency, Reliability, and Flexibility Solutions
Grid Stability, Reliability, and Resiliency
  Storms and natural disasters are growing in frequency, scale, and cost
  Mounting demand from ratepayers, regulators, and utility leadership for improved grid performance
  S&C Electric estimates that 90% of outages occur on the distribution grid
  Current methods of outage management (truck rolls and customer call-ins) are ineffective and costly
  Community restoration is largely dependent on successful and swift power grid restoration
DER Integration Challenges
  Voltage Instability
  Bidirectional Power
  Fluctuating Power Quality
  Capacity Constraints
  DG Load
Aging Distribution Assets
  Smart storm reconstruction processes and technologies will prevent future failures
  Most distribution grid assets in North America are 25-50 years old, and require replacement even without storm risks
  Standard practice has been to replace failing assets or wait for it to reach the end of its useful life
  Utilities typically choose between retrofit and replace if an asset is not destroyed – in either case, the best available technologies should be deployed if possible
Progressive Ratemaking Strategies
  Transition away from cost-of-service ratemaking is slowly occurring
  Smart reconstruction investment can vastly improve reliability metrics, bringing tangible financial benefits to utilities
  Utilities are expected to deliver reliable power, and are fined or rewarded based on their performance.
Market Drivers

## Slide 7: Disaster Management
Three Phases for Success
Predict, Prepare, and Protect
Withstand and Mitigate
Respond and Recover
The best way for utilities and network providers to mitigate outages and operate a resilient grid is to proactively and preemptively invest in hardware and software technologies in preparation for weather and other outage events.
As the effects of the disaster pile up, the consequences of utility investment (or lack thereof) in prediction, preparation, and protection strategies will directly and adversely affect its response actions during the withstand and mitigate phase.
The respond and recovery phase heavily relies on system visibility maintained by the utility throughout the event. With advanced remote monitoring and automation, a utility will know which key assets have been affected and will dispatch response crews or manually reroute power as needed.
Once direct recovery from a disaster is complete, a utility must spend time reviewing what worked, what did not, and what could have been done differently or prevented. Update the plan as equipment is bought, upgraded, changed, or repaired.

## Slide 8: Strategic and Cost-Efficient Resiliency Strategies
Storms are increasing in strength and frequency
The technology is here, and it is up to utilities to use it
Utility siloes are being broken
Community resiliency is tied to grid restoration
02
Flexibility Enables Balanced Solutions
Utilities must have a flexible mindset when working toward achieving the goal of high reliability driven by smart storm restoration strategies and technologies. With flexible systems and an innovative approach, grid performance will improve markedly, even considering the increase in natural disasters.
04
Future-Proofing Requires Constant Re-Evaluation
Utilities must not rest with current systems, technologies, protection schemes, or recovery efforts. Instead, they must continually and systematically improve all aspects of grid hardening and resiliency across their T&D networks
Strategic Planning and Investing
Thinking Ahead Ensures Preparedness
When planning for current and future grid investment, it is critical that utilities take a holistic view of their network’s key weaknesses and issues that need to be addressed, now and in the future, and weigh the costs and benefits of resiliency technologies versus the results of inaction.
03
Collaboration Breeds Innovation
With collaborative efforts on the part of both the utility and their solutions provider, innovation across and within segments and groups will provide utilities with more, superior solutions than they may be able to purchase off the shelf or build themselves
01

## Slide 9: Key Storm Reconstruction & Resiliency Technologies
Rebuilding the electric power system must incorporate innovative smart grid solutions – information and communications technologies with built-in computing power and automation, such as smart meters and distributed and connected sensors – to isolate problems and bypass them automatically. These technologies provide resilience and flexibility to grid operators and help power restoration efforts after a storm.
When power interruptions occur, microgrids, energy storage, and other distributed and backup generation systems can ensure continued operation of critical facilities.
For critical equipment, cabling resistant to long-term submersion in water and oil and other pollutants potentially present in flood waters should be used. In addition, classes of transformers, switches, and enclosures that are designed to be submersible should be deployed in flood-prone areas
After a disaster, power should be restored to the most critical services first. Planning efforts should also carefully consider safety issues that can emerge when recovering from flooding.
Distribution Automation & FLISR
Distributed and Backup Generation
Software Platforms
Grid Monitoring and Control
Microgrids
Hardened Grid Assets
Smart Meters
Energy Storage
Building a Smarter Grid

## Slide 10: Wildfire Mitigation Technologies
With much of the world’s electric infrastructure built as overhead lines with wooden poles, the risk of major network destruction and outages resulting from wildfires is high. Beyond mitigating wildfire damage should a fire occur, it is critical that utilities take actions and deploy technologies onto their networks to prevent wildfire ignition due to asset failure, vegetation management, and other scenarios.
A self-healing grid with strategically placed intelligent switches, relays, reclosers, and other devices will increase fault recognition speed and network safety. In the event of an ignition risk on the network, a FLISR system can ensure power is cut to at-risk locations and routed through healthy networks.
T&D substation monitors with asset health information and operating condition monitors and can detect outages and ignition conditions. Ambient temperature sensors may also determine if an asset is failing due to fire or if the asset temperature is high enough to promote ignition.
As much as 50% of utility-caused wildfires begin as a result of vegetation coming into contact with energized lines. Utilities can leverage advanced vegetation management schemes to drastically reduce wildfire ignition risk. VM platforms can autonomously scan images, and using AI and machine learning, recognize network and asset characteristics indicative of high-risk vegetation growth.
Microgrids will become a key source of backup local generation for when centralized power goes out. Outages that result from wildfires can be restored by connection to a microgrid, and preventative outages, such as the rolling blackouts conducted in California in the summer of 2020 to mitigate wildfire risk, can be offset with microgrids and DG to maintain power through planned outage scenarios.
AMI meters and smart sensors can communicate with utilities to provide updates on network conditions. During wildfires, this information can be used for firefighting operations and to ensure that power has been cut to at-risk locations. Sensors and some meters can detect voltage fluctuations that may be indicative of outages or ignitions on connected segments of a T&D network.
A grid management platform can help utilities manage outages, manually or automatically reroute power, and cut power to areas of the system with high ignition risk. These system can pull in data from distributed sensors—for example, wind or temperature sensors out on transmission lines—and help utilities take the appropriate and safest action.
1
FLISR, Reclosers & Sectionalizers
2
Remote Substation Monitoring
3
Vegetation Management
4
Microgrids and Distributed Generation
5
Smart Meters, Line Monitors, and Sensors
6
ADMS, OMS, EMS, SCADA

## Slide 11: Key Conclusions and Recommendations
Build the Grid of Tomorrow
The energy and utility industry is deeply entrenched in a dynamic period of innovation and disruption at all levels. Many utilities are shifting away from sole reliance on central generation, while customers manage their energy usage like never before.
The intersection of data availability and advanced computing power has put holistic grid infrastructure management within sight, and utilities must act.
Building for tomorrow includes preparing a communications infrastructure that can handle vast and advanced software platforms and manage severe outage events across an entire grid network
Most importantly, the deployment of smart technologies and connected assets on the grid itself before, during and after a storm or natural disaster will allow utilities to operate and maintain a high-performing grid for years to come.
Continue to Innovate to Address Resiliency Challenges
Recognizing modern growth opportunities is a critical factor for business growth, but understanding the needs of the next-generation reliable utility and providing innovation and product development to meet those needs is equally important.
The most successful vendors in the resiliency technologies space will be those that continue to drive innovative solutions forward, demonstrating the benefits to utilities, regulators, and ratepayers.
As the frequency and intensity of storms and other hazards natural disasters grows, so too should the pace of innovation and the rate of deployment
As unidirectional power flows morph into interconnected, intelligent, and self-healing machines with energy and information flowing from asset to asset in all directions, vendors must lead the charge and ensure cutting-edge smart energy technologies are integrated safely and securely and facilitate and secure the next generation of grid reliability and resiliency.
Consider and Prioritize Flexible Options
Every utility is unique in its strengths, challenges, climate, and regulatory landscape. This means every product and every project should be developed and deployed to match specific needs.
Utilities that struggle with wildfires in California will need different resiliency technologies and equipment than those in Florida seeking assistance with hurricane restorations.
Among the most important flexible and dynamic storm restoration technology categories include device hardware, networking, communications, IT and analytics platforms.
This type of flexibility will keep the market growing and allow vendors across the segment to witness success and utility networks to prepare, withstand, and recover from storms stronger than ever before.
Storm Restoration Technologies and Strategies for Utilities & Vendors

## Slide 12: DER Integration

## Slide 13: Table of Contents
Introduction
Why DER?
  Technical Standards Considerations
Key Recommendations
Contacts
Regulatory and Statutory Considerations

## Slide 14: Introduction
The energy transformation is being propelled by growing customer demand for cleaner, more flexible, and cheaper solutions. This evolution will go well beyond the power grid and the power industry—it will affect the way we live, work, and move in our communities, as well as the way we use materials, produce and move goods, and provide services.
Distributed energy resources (DER) are an integral part of this transformation. They provide an economic and resilient solution to energy consumers at the grid edge. To cope with the increasing number of DER assets deployed and to ensure these are treated as equal within the power system, utilities, regional transmission organizations (RTOs), independent system operators (ISOs), and the federal government are implementing grid interconnection guidelines that DER installations need to follow. This report highlights the type and main characteristics of the regulations being implemented.
Electrical equipment manufacturers will also need an overview of the process that DER installations need to follow to get interconnected. This report discusses how NEMA members’ product can help installers simplify their interconnection processes by getting equipment certifications and following the required standards.
Finally, the report goes beyond DER interconnection requirements and shows how DER and equipment manufacturers can play an extended role in the future power system. Use cases showcase how equipment manufacturers and utilities can partner to create the right structure to capture all the value that DER can provide to customers, the grid, and ultimately, manufacturers.

## Slide 15: Table of Contents
Introduction
Why DER?
  Technical Standards Considerations
Key Recommendations
Contacts
Regulatory and Statutory Considerations

## Slide 16: North America DG Deployment Market Forecast
Analyst Insights
In North America, the need for resilience and deployments of distributed solar PV and solar plus storage should continue to drive demand for DER solutions across all major US states. Despite a short-term decline in DG deployments, decarbonization and clean technology pushes across major economies and regulatory bodies should encourage greater offset of DG for centralized generation technologies. According to Guidehouse Insights’ estimates, new DG deployments should continue to exceed the deployment of new centralized generation capacity growth.
Cumulative DG Capacity by Technology, North America: 2020-2030
Annual Total DER Capacity by Region, World Markets: 2020-2030
Note: Regulatory changes from the new US administration not included
Chart: (MW)
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Diesel Gensets | 159835.1623 | 160409.7792 | 183435.2778 | 184295.015 | 185182.3722 | 186009.645 | 186847.1716 | 187757.4981 | 188740.1376 | 189673.6451 | 190508.6247
Solar | 41540.3913 | 51643.0657 | 63843.7461 | 77157.5621 | 92804.905 | 111101.928 | 130967.5455 | 152929.9509 | 177199.5504 | 203479.5185 | 231725.7746
NG Gensets | 43250.8653 | 45987.2599 | 54699.9961 | 58232.8933 | 61974.6234 | 65875.2274 | 70000.4593 | 74423.0027 | 79171.2898 | 84020.9399 | 88980.4362
Wind | 2968.7405 | 3148.6818 | 3330.4224 | 3513.9805 | 3699.3742 | 3886.6217 | 4075.7418 | 4266.7531 | 4459.6744 | 4654.525 | 4851.3241
Other Renewables | 2102.43 | 2194.83 | 2293.83 | 2399.43 | 2505.03 | 2613.93 | 2745.93 | 2877.93 | 3016.53 | 3161.73 | 3313.53
Stationary Fuel Cells | 632.6295 | 725.0315 | 824.7415 | 931.9522 | 1046.159 | 1166.6676 | 1290.029 | 1413.7464 | 1537.6127 | 1661.6313 | 1785.8056
Microturbines | 391.5947 | 428.4419 | 536.2601 | 585.9357 | 639.8483 | 698.392 | 761.9761 | 831.0468 | 906.0961 | 987.6534 | 1076.2959

## Slide 17: DER Market Overview
The North America DG market is increasing at a CAGR* of 9.7% until 2030.
Market challenges will result in 19.1 GW of DG capacity additions in 2020.
North American cumulative DG capacity is estimated to exceed 522 GW by 2030.
North America is expected to install 18.2% of the world's new DG from 2020-2030.
Despite supply chain hurdles, 5.7 GW of North America’s DG will come from solar PV in 2020.
C&I customers will account for 70.9% of DG capacity in 2020.
North American DG revenue is expected to reach $350 billion between 2020-2030.
* See the acronyms and abbreviations list for spellouts.
The US is expected to account for 94.6% of North America's DG growth between 2020 and 2030.

## Slide 18: The DER Value Chain
Despite the impacts of the pandemic, DER generation technologies still benefit from being mature markets and are likely to have greater resiliency to restrained market conditions than some other DER technologies. Additionally, generation technologies are often the go-to choice for reliable and cost-effective power, especially in regions with more outages.
Technologies | Diesel Gensets Natural Gas Gensets Stationary Fuel Cells Microturbines | Solar PV Wind Other Renewables (Biogas/Biomass) | DR DERMS | DESS Thermal Storage | EV Charging Energy Efficiency HVAC
DER Value Chain
Storage
Energy Efficiency and Load
Distributed Generation
Conventional
Renewable
Distribution and DSM
The C&I sector is expected to be most heavily affected in the current market conditions due to decreased activity and corresponding economic effects. Different regions are predicted to have different levels of effects, with nascent markets taking less of a direct hit than established markets; regions containing pandemic hotspots are expected to be more heavily affected. Application segments with stimulus packages that incentivize clean energy are likely to bounce back more rapidly.
Key Highlights across the Value Chain

## Slide 19: Market Inflection Trends
 | Northeast US | Southern US | Midwest US | West US | Canada
Short- to medium-term growth potential (2020–2025) | High | High/ Moderate | Moderate | High | Low
Long-term growth potential (2025–2030) | High/ Moderate | High | High/ Moderate | High | Moderate
Market uncertainty | Low | Moderate | Moderate | Low | High
DG Deployment: Industry Growth Potential, North America
Analyst Insights
With the ongoing energy transition, customer needs are evolving to accommodate the demand for implementing efficient DER solutions. This trend is motivating producers and consumers of distributed power to look beyond traditional generation and specific project finance instruments and into new and innovative solutions. In the US, the new Biden administration is likely to encourage growing climate change efforts by local states with federal support.
Shifting utility incentive structures are beginning to push utilities to more efficiently adopt distributed resources, which should increase adoption in many locations across the country.
The recession spurred by COVID-19 has decreased demand and investment for distributed generation projects. This trend will likely continue through 2021.
Favourable legislation, such as FERC Order No. 2222 and president-elect Biden’s support for the Clean Energy Revolution, should ease the integration of clean and distributed generation technologies into the grid.
Increased demand for resiliency resulting from widespread forest fires in the western US will fuel distributed generation adoption.

## Slide 20: Market Drivers and Barriers
Market Drivers
1–2 years
3–4 years
5–7 years
Clean energy policy under the new Biden administration and wholesale market reform
Increased demand for resiliency in the western US
Proper incentives for utilities, such as New York’s earning adjustment mechanisms
DG allowing utilities to delay T&D upgrades and defer infrastructure costs
Impact: High Medium Low
7–10 years
Impact over the Next 10 Years
Market Barriers
Global deployments of generation technologies impacted by COVID-19 in the short term
Renters and condo owners, a substantial market segment in North America, having limited access to DG
Regulatory barriers on PPAs limiting DG growth in some states such as Kentucky
Managing the intermittency of DG, especially at high penetrations, requiring investment in costly DSM solutions

## Slide 21: Table of Contents
Introduction
Why DER?
  Technical Standards Considerations
Key Recommendations
Contacts
Regulatory and Statutory Considerations

## Slide 22: Regulatory and Statutory Considerations for Successful DER Integration
Federal
Regional and State Level (ISO/RTO and Distribution Level)
Individual Utility Considerations
DER Interconnection regulations can come from the Federal or State Governments, RTO/ISO or individual utilities.
Traditionally, Most regulations regarding DER integration are set at the regional or state regulatory level. But the Federal government is becoming increasingly active in the space.
Individual utilities translate high-level regulation in practical interconnection processes and set technical requirements

## Slide 23: Regulatory and Statutory Considerations for Successful DER Integration
FERC Order No. 2222: The FERC issued a breakthrough order on September 17, 2020. This order adopted rules aimed at removing barriers to the participation of DER in organized markets for electric energy, capacity, and ancillary services operated by regional transmission organizations (RTOs) and independent system operators (ISOs).
DOE Support: Despite not being a top priority of federal energy policy, the DOE continues to support renewable energy, efficiency programs, DR, and DER. In 2018, DOE allocated an estimated $860 million to support energy efficiency, renewable energy, and clean transportation research and development.
Federal
Regional and State Level (ISO/RTO and Distribution Level)
Individual Utility Considerations

## Slide 24: Regulatory and Statutory Considerations for Successful DER Integration
Federal
Regional and State Level (ISO/RTO and Distribution Level)
Individual Utility Considerations
North American ISOs and RTOs and State legislations are all at varying stages of DER integration. As DER technologies proliferate across the continent, they can provide capacity and ancillary services to the regional markets. However, these technologies will require their own set of rules when compared to traditional fossil generation.
Some of the most important aspects of regional legislation are:
  Renewable Energy Goals Status
  Distribution Deferral Opportunities
  Building Regulation
  Capacity Markets Rules

## Slide 25: Regulatory and Statutory Considerations for Successful DER Integration
Federal
Regional and State Level (ISO/RTO and Distribution Level)
Individual Utility Considerations
DER integration strategies vary from utility to utility depending on the local DER penetration, grid constraints, decarbonization strategies, and regulator push to support DER or for new strategies of grid constrain management.
DER integration practices cover a wide range of activities—from the interconnection of DER to the grid, to DER program planning and deployment, measurement and verification, and settlement.
Individual utilities develop their own rules and processes to manage the interconnection of DER assets into their grid.
Hosting capacity evaluations and DR and DER Programs are the two main ways in which utilities manage DER and their interconnections.
DER interconnections are usually evaluated for the following:
  Safety of the general public or utility personnel
  Risk of degradation to services for customers due to interruptions or power quality events
  Compromise of security or reliability of electrical systems

## Slide 26: Typical DER Interconnection Process
The technical review is the most important aspect from an equipment manufacturer point of view. A technical review of each interconnection application is generally made to confirm the operation of the proposed DER system is consistent with the technical requirements of the power delivery system and does not adversely impact other customers.
Application submittal
Technical review
Conditional approval
Construction
Inspection
Testing
Permission to operate
The following are the most common requirements evaluated during the technical review process:
  Protection requirements
  Stability studies
  Metering requirements
  Telemetry requirements
  Asset Access requirements

## Slide 27: Table of Contents
Introduction
Why DER?
  Technical Standards Considerations
Key Recommendations
Contacts
Regulatory and Statutory Considerations

## Slide 28: Technical Standards Considerations
The main standards used for DER interconnection are:
  IEEE 1547-2018
  IEEE 1815 (DNP3)
  IEEE 2030.5 (SEP 2.0)
  UL 1741 (Inverter Performance Standards)
  Smart Inverters (California Rule 21)
  OpenADR 2.0
  SunSpec Modbus
Over the last decade, work on standards was focused on ensuring that DER connected to the grid does not pose a risk to the grid stability. Today, the standardization process is going beyond that and is increasingly focused on providing a communication layer that enables more complex interaction between DER and the grid.

## Slide 29: Table of Contents
Introduction
Why DER?
  Technical Standards Considerations
Key Recommendations
Contacts
Regulatory and Statutory Considerations

## Slide 30: Key Conclusions and Recommendations
Realigning strategic focus and reevaluation of business models can unlock new opportunities.
Prosumers are at the center of the DER ecosystem. This transition of decision-making into the hand of the consumers can be an opportunity rather than a limitation for energy stakeholders. Energy providers should realign their strategic intent in the new normal and shift their operating models to identify the best aggregation strategies with their customers. A service-oriented business model can offer a win-win solution across stakeholders.
Utilities should realize and embrace opportunities across DER models.
Utilities should help create a competitive energy market by working with regulators to create the most efficient rate design. Especially considering recent FERC Order No. 2222, which requires most utilities to accept DG in wholesale markets, DG is here to stay. Utilities should push for time and location varying rates as an alternative to net metering.
OEMs need to be aware of the interconnection process and the standards required
Understanding the interconnection process and providing information and tools that help installers and project developers reduce the effort needed to get assets interconnected is a ley competitive advantage
For electrical equipment manufacturers and digital DER management tool providers, it is critical that their products support or are planning to support the technical standards to remain relevant in the marketplace.

## Slide 31
Michael Hartnack Senior Research Analyst Michael.Hartnack@Guidehouse.com
Erik Gilbert Director erik.gilbert@guidehouse.com
Brett Feldman Associate Director Brett.Feldman@Guidehouse.com
Roberto Rodriguez Labastida Senior Research Analyst roberto.rodriguez.labastida@guidehouse.com
Questions?